*********************Default*********************
Catboard-Pipelinec
PMOD-Ethernet
02/21/25
*********************Default*********************

pico-ice 12MHz Catboard 100MHz
pmod-ether 25MHz

/**
 * PLL configuration
 *
 * This Verilog header file was generated automatically
 * using the icepll tool from the IceStorm project.
 * It is intended for use with FPGA primitives SB_PLL40_CORE,
 * SB_PLL40_PAD, SB_PLL40_2_PAD, SB_PLL40_2F_CORE or SB_PLL40_2F_PAD.
 * Use at your own risk.
 *
 * Given input frequency: 100.000 MHz
 * Requested output frequency: 25.000 MHz
 * Achieved output frequency: 25.000 MHz
 */

.FEEDBACK_PATH("SIMPLE"),
.DIVR(4'b0000),	// DIVR = 0
.DIVF(7'b0000111),	// DIVF = 7
.DIVQ(3'b101),	// DIVQ = 5
.FILTER_RANGE(3'b101)	// FILTER_RANGE = 5

pico-ice to catboard
# PMOD0A
set_io -nowarn ICE_45 45
set_io -nowarn ICE_47 47
set_io -nowarn ICE_2 2
set_io -nowarn ICE_4 4

# PMOD0B
set_io -nowarn ICE_44 44
set_io -nowarn ICE_46 46
set_io -nowarn ICE_48 48
set_io -nowarn ICE_3 3

# pin definitions
set_io d7_o A15
set_io d0_o A11
set_io d5_o B13
set_io d6_o B15
set_io d2_o B12
set_io d3_o B11
set_io d1_o B10
set_io clk_i C8
set_io d4_o B1

xx

xx